## Slide 1: Advance Algorithm Summer Session project
Retiming of a graph

## Slide 2: Retiming problem
Problem
Optimize the frequency of a circuit
Solutions
Move register(s) so that
clock cycle decreases, or number of registers decreases and
input-output behavior is preserved

## Slide 3: Circuit Representation
Example: Correlator (from Leiserson and Saxe) (simplified)
Circuit
(x, y) = 1 if x=y
0 otherwise
Operation delay
 3
+ 7
Every cycle in Graph has at least one register i.e. no combinational loops.
0
3
3
0
0
0
0
2
Retiming Graph (Directed)
7
a
b
+

Host


## Slide 4: Circuit Representation
Circuit represented as retiming graph G(V,E,d,w)
  V  set of gates
  E  set of connections
  d(v) = delay of gate/vertex v, (d(v)0)
  w(e) = number of registers on edge e, (w(e)0)

## Slide 5: Clock Cycle
For a path p :
Clock cycle
For correlator c = 13
Path with
w(p)=0
0
3
3
0
0
0
0
2
7

## Slide 6: Retiming for Minimum Clock Cycle
  Problem Statement: (minimum cycle time)
  Given G (V, E, d, w), find a legal retiming so that
  is minimized

## Slide 7: Implementation details
Reference paper:
  C. E. Leiserson and J. B. Saxe, "Retiming Synchronous Circuitry", Digital Systems Research Center, Report 18, August 20, 1986.
  Implement Algorithms: WD, OPT1, FEAS and OPT2
Use BGL – Boost Graph Library to describe the Retiming Graph
  https://www.boost.org/doc/libs/1_67_0/libs/graph/doc/index.html
Testcases: random generated retiming graph
Python vs C++
Anti plagiarism software – Honor code
Share a GitHub repo. Private repo are free for students

## Slide 8: Evaluation
How it is presented
How it is documented
How it is tested
How it is assessed

## Slide 9: AAPP exam
From the exam rules:
It is possible to integrate or to partially skip the written exam with either a programming project or a report on further readings
  Project on parallelization -> skip II part
  Project on advanced algorithms -> skip I part
In case you pass this take-home project, you will skip the I part of the exam